## Slide 1: Examining the Hydrologic Properties of the Missouri River Basin
Rachel Bash, Keqi He, Caroline Watson, Haoyu Zhang

## Slide 2: Study Rationale
Largest river in N.A.; 2nd largest watershed.
Large proportion of agricultural lands.
Nutrient enrichment & water impairment
Map Layers Sources:
Land use: GAP/LANDFIRE National Terrestrial Ecosystems 2011;
Impaired waters: EPA ATTAINS (cf. Clean Water Act 303d List 2015)
Watersheds & streams: USGS
Notes: Hubert ~ 1min
As you may have known, the Missouri River is the largest river in North America, and it also has the second largest watershed of 338 million acres including a small part in Canada.
The basin is primarily rural, but also has several large or medium-sized cities. As shown on this map, a large proportion of the region is agricultural land. 218 acres are related to agriculture, and two major land uses are cropland and pasture.
Across the whole basin, agricultural lands are the predominant source for nutrient loading into water bodies. According to Clean Water Act 303 d list 2015, more than 160 waterbodies are impaired due to nutrient enrichment.
Since most of agricultural lands are located in the lower Missouri basin, in this project we focused on sub-basins in the southeast.

## Slide 3: Our Research Questions
How have changes in discharge (i.e. water quantity) interacted with nutrient enrichment (i.e. water quality) in the Missouri River Basin?
a) Nutrient levels have increased over time
b) Discharge has become more variable over time
c) Nutrient levels increase with discharge
What effects do specific flood and drought events have on the water quality and quantity of rivers in the Missouri River Basin areas of interest?
a) Rivers will exhibit a flushing behavior due to the land use and type of flow during storms
b) Discharge will decrease during drought due to decreased overland flow.
What factors contribute to the variability of total nitrogen in the rivers?
a) Land use, year, discharge, phosphorus, and HUC region will contribute to the variability of total nitrogen across sites
Given past and current data, what can we predict about the future state of water in the Missouri River Basin?
a) Total flow in the Missouri River Basin is increasing (non-stationary) over time
b) The future situation of the river basin will see the continuation of current trends of increasing overall volume of flow.
Notes: caroline

## Slide 4: Our Approach
22 sites chosen throughout HUCs 1020 – 1030
  2 sites per HUC
Nitrogen, Phosphorus, Discharge, Time
Notes: Caroline

## Slide 5: Dataset Information
Source: The United States Geological Survey (USGS) database
National Water Information System (NWIS) https://waterdata.usgs.gov/nwis
Steps:
  Filter sites in HUC 1020 - 1030 to only show us sites that contained discharge, nitrogen, and phosphorus data.
  Choose 2 sites from each HUC sub basin for a total of 22
  By comparing the periods of records for each chosen variables and finding the sites with the longest periods of records.
  Two sites per HUC region: maintain a digestible scope.
Notes: keqi

## Slide 6: Exploratory Analysis
Day of year
Notes: rachel

## Slide 7: Q1: How have changes in discharge (i.e. water quantity) interacted with nutrient enrichment (i.e. water quality) in the Missouri River Basin?
Seasonal Mann-Kendall Trend Test
  N: 7 increase; 7 decrease
  P: 7 increase; 5 decrease
  Mainstem increasing
Discharge × nutrient
  18/22 positive relationship
Notes: Hubert ~2min
To investigate the trend of nutrient concentration, we used long-term daily values and seasonal Mann-Kendal test. Among all 22 sites, 7 sites show significantly increasing trends in nitrogen concentration, while 7 show decreasing trends. For phosphorus, concentrations at 7 sites have increased over time, while decreased at other 5 sites. Despite inconsistent results at all sites, those on the mainstem show higher nutrient concentration, such as 7, 10, and 22.
We further examined the interaction between discharge and nutrient concentration. High-freq data were used for sites where the data are available, and for all other sites daily values were used. The relationship was analyzed by linear model with total nitrogen as the response variable and discharge as the explanatory variable.18 out of the 22 sites show a significant positive relationships.

## Slide 8: Q2: What effects do specific flood and drought events have on the water quality and quantity of rivers in the Missouri River Basin areas of interest?
Notes: Caroline

## Slide 9: Q3: What factors contribute to the variability of total nitrogen in the rivers?
Fixed effects: Year and population
Random effect HUC 4 area
Exponentiating the coefficients produces integers with multiplicative effects on nitrogen
Discharge was not significant
Notes: Rachel

## Slide 10: Q4: Given past and current data, what can we predict about the future state of water in the Missouri River Basin?
Mann-Kandall Trend Test
Autoregressive and Moving Average Models (ARMA)
AR part: involves regressing the variable on its own lagged (i.e., past) values
MA part: involves modeling the error term as a linear combination of error terms occurring contemporaneously and at various times in the past
Notes: Keqi

## Slide 11: Conclusions